## Slide 1
VLSI Physical Design Implementation of a Post-Quantum Cryptographic Accelerator SoC
Project Guide: Dr. Velmathi G.
Team Members:
Subham Prasad Gupta (23BVD1039)
Jairus Solomon Samraj (23BVD1040)
Vinayak Shreenivas Salunke (23BVD1062)

## Slide 2
Implementation Work Distribution
Subham | Jairus | Vinayak
Modular Arithmetic | Polynomial Processing | Keccak / SHAKE
NTT / INTT | Matrix-Vector Multiplication | Sampling
Pointwise Polynomial Multiplication | Compression / Decompression | Matrix Generation
Transform Datapath | ML-KEM Control | Encryption
Arithmetic Optimization | KeyGen / Decapsulation | Cryptographic Datapath
Arithmetic Pipelining | SoC Integration | Encryption Pipelining
Synthesis & Timing Analysis | Baseline Synthesis | Final Pipeline Optimization
RTL to Synthesis Work Distribution

## Slide 3
Arithmetic & Transform Engine (Subham)
Modular Arithmetic
  mod_add.v
  mod_sub.v
  mod_mult.v
  mod_mult_top.v
  mod_reduce_3329.v
NTT
  ntt.v
  ntt_butterfly.v
  ntt_memory.v
  ntt_zetas_rom.v
  ntt_flat.v
INTT
  intt.v
  intt_butterfly.v
  intt_scheduler.v
  intt_zetas_rom.v
  intt_flat.v
Polynomial Multiplication
  poly_mul_pointwise.v
Responsibility
Implementation of ML-KEM modular arithmetic and NTT/INTT transform datapaths, including polynomial multiplication in the NTT domain. Evaluated the initial pipelined architecture at 50/100 MHz and performed the 250-MHz stress test on the final pipelined architecture.
Run | Frequency | Purpose
Run 1 | 50MHz / 180nm | Initial timing evaluation
Run 2 | 100 MHz / 90nm | Timing eval at target freq
Pipeline Type 1 — Initial Pipelined Architecture
Run | Frequency | Purpose
Run 3 | 250MHz | High-frequency stress test
Pipeline Type 2 — Final Architecture

## Slide 4
Arithmetic Datapath Pipelining: poly_mul_pointwise.v
Original critical path:
mod_mult
↓
mod_mult
↓
mod_add
Pipeline modification:
STAGE 1
4 × mod_mult
↓
PIPELINE REGISTERS
↓
STAGE 2
mod_mult + mod_add
Code-level changes
Declarations
  Added stage1_valid
  Added stage2_valid
  Added Stage-1 → Stage-2 registers:
    p_a0b0_r
    p_a1b1_r
    p_a0b1_r
    p_a1b0_r
    gamma_r
    idx_i_r
Datapath
  Separated the second mod_mult from the first stage.
  p_gamma now operates on registered p_a1b1_r.
  Final mod_add operates after the pipeline boundary.
Control
  Added valid propagation:
    stage1_valid
    stage2_valid
  Modified COMPUTE state to:
    Capture Stage-1 results.
    Propagate valid.
    Perform Stage-2 writeback.
Reset
  Added reset initialization for all new pipeline registers and valid signals.
Latency
  Total operation increased to approximately 129 cycles, only one additional cycle relative to the previous implementation.
Notes: Post-quantum cryptography refers to cryptographic algorithms designed to resist attacks from quantum computers while still running on conventional computing systems. This is important because the cryptography does not itself require a quantum computer. NIST has already standardized ML-KEM for key encapsulation and ML-DSA and SLH-DSA for digital signatures. For our hardware accelerator, we are particularly interested in lattice-based cryptographic computation, especially the computational kernels associated with ML-KEM.

## Slide 5
Arithmetic Datapath Pipelining: mod_reduce_3329.v
Original critical path:
value × MU
↓
quotient estimation
↓
quotient × Q
↓
remainder
↓
conditional reduction
Code-level changes to mention
Depending on the exact pipelined revision you used, the changes should include:
  Added clock/reset interface
  Added registers for the reciprocal multiplication result
  Registered the quotient estimate
  Registered intermediate quotient/product values
  Separated the Barrett reduction into multiple sequential stages
  Added valid/control propagation if the surrounding datapath required it
  Reset all newly introduced pipeline registers
  Updated downstream timing/latency expectations
Purpose
Break the long Barrett-reduction combinational path into shorter arithmetic stages while preserving modulo-3329 functionality.
Pipelined:
STAGE 1 STAGE 2
value × MU → REGISTER → quotient estimation → REGISTER → quotient × Q → remainder → conditional reduction
Notes: Post-quantum cryptography refers to cryptographic algorithms designed to resist attacks from quantum computers while still running on conventional computing systems. This is important because the cryptography does not itself require a quantum computer. NIST has already standardized ML-KEM for key encapsulation and ML-DSA and SLH-DSA for digital signatures. For our hardware accelerator, we are particularly interested in lattice-based cryptographic computation, especially the computational kernels associated with ML-KEM.

## Slide 6
CODE-LEVEL PIPELINE SUMMARY
poly_mul_pointwise.v
Added
p_a0b0_r
p_a1b1_r
p_a0b1_r
p_a1b0_r
gamma_r
idx_i_r
│
▼
stage1_valid → stage2_valid
Timing objective:
Break the multiplier cascade and reduce the arithmetic critical path.
The source comments in your current RTL describe the intended improvement as approximately:
~14 ns → ~5 ns
which is useful as an RTL-level timing target/analysis point, but distinguish it from the final Genus WNS results.
Notes: Post-quantum cryptography refers to cryptographic algorithms designed to resist attacks from quantum computers while still running on conventional computing systems. This is important because the cryptography does not itself require a quantum computer. NIST has already standardized ML-KEM for key encapsulation and ML-DSA and SLH-DSA for digital signatures. For our hardware accelerator, we are particularly interested in lattice-based cryptographic computation, especially the computational kernels associated with ML-KEM.

## Slide 7
Polynomial/Vector Processing & System Control (Jairus)
Polynomial Operations
  poly_add.v
  poly_sub.v
Matrix / Vector Datapath
  matrix_vec_mul.v
Compression / Representation
  poly_compress.v
  poly_decompress.v
SoC Integration
  mlkem_peripheral.v
  mlkem_picosoc_top.v
ML-KEM Control
  mlkem_top.v
  mlkem_keygen.v
  mlkem_dec.v
Responsibility
Polynomial/vector processing, ML-KEM operation control and integration of the accelerator with the PicoSoC/PicoRV32 system. Decouple pointwise multiplication from the following parallel polynomial-addition paths.
Run | Frequency / lib | Purpose
Baseline 1 | 100 MHz / 90nm | Initial synthesis
Baseline 2 | 100 MHz / 90nm | Timing characterization
Pipeline Type 1: No-Pipeline ML-KEM
System Integration
  PicoRV32 ↔ PicoSoC ↔ ML-KEM peripheral
  Memory-mapped control/status interface
  ML-KEM operation sequencing
Additional work
Initial synthesis debugging, Datapath error correction, Baseline timing analysis, Critical-path identification, SDC/constraint debugging.

## Slide 8
MATRIX-VECTOR PIPELINING: matrix_vec_mul.v
Original critical path:
poly_mul_pointwise
↓
256-coefficient poly_add
↓
256-coefficient poly_add
Pipeline modification:
poly_mul_pointwise
↓
REGISTER
↓
poly_add
↓
poly_add
Code-level changes
New registers:
prod_A00_s0_r
prod_A01_s1_r
prod_A10_s0_r
prod_A11_s1_r
New control signal:
pm_start2
FSM modified
Original row processing was reorganized into:
IDLE → ROW0 → LATCH_ROW0 → ROW1 → LATCH_ROW1 → FINISH
Sequential changes:
  Capture row-0 multiplication outputs into registers.
  Start row-1 processing in a separate state.
  Capture row-1 outputs.
  Delay done until both registered results are available.
Reset changes:
  Initialize all four holding registers.
  Initialize pm_start2.
Objective:
Decouple pointwise multiplication from the following parallel polynomial-addition paths.
Notes: Post-quantum cryptography refers to cryptographic algorithms designed to resist attacks from quantum computers while still running on conventional computing systems. This is important because the cryptography does not itself require a quantum computer. NIST has already standardized ML-KEM for key encapsulation and ML-DSA and SLH-DSA for digital signatures. For our hardware accelerator, we are particularly interested in lattice-based cryptographic computation, especially the computational kernels associated with ML-KEM.

## Slide 9
Cryptographic Datapath (Vinayak)
Matrix Generation
  mlkem_matrix_gen.v
ML-KEM Encryption
  mlkem_enc.v
Encoding / Decoding
  poly_encode.v
  poly_decode.v
Keccak / SHAKE
  keccak_f1600.v
  shake128_xof.v
Sampling
  cbd_sampler.v
  rejection_sampler.v
  poly_uniform.v
Contribution
Implementation of cryptographic primitives, sampling, matrix generation and the ML-KEM encryption datapath. Final pipeline architecture, Timing-driven RTL restructuring, Final mlkem_enc pipeline implementation, Synthesis/timing evaluation, Achieved 0-slack operation at 100 MHz
Run | Frequency / lib | Purpose
Run 1 | 100MHz / 45nm | Test run at lower process parameter
Run 2 | 100 MHz / 90nm | Timing evaluation at target frequency
Pipeline Type 2 — Final Architecture

## Slide 10
ENCRYPTION PIPELINING: mlkem_enc.v
Original critical path:
NTT
↓
Matrix-Vector Multiplication
↓
INTT
↓
Polynomial Addition
↓
Compression
The INTT completion path was followed directly by:
  poly_add(e2)
  poly_add(message)
  768 parallel poly_compress units
This created a long combinational path.
Pipeline modification
INTT
↓
u0/u1/v REGISTER
↓
RUN_COMPRESS
↓
Compression
Code-level changes:
New holding registers
u0_spatial_r
u1_spatial_r
v_final_r
Compression inputs changed:
Previously: u0_spatial, u1_spatial, v_final
Compression now operates on:
u0_spatial_r, u1_spatial_r, v_final_r
New FSM state:
RUN_COMPRESS
IDLE
↓
RUN_NTT
↓
RUN_MVM
↓
RUN_INTT
↓
RUN_COMPRESS
↓
FINISH
Objective
Isolate the compression logic from the INTT/message-addition timing path.
The RTL comments identify an approximately 5-ns critical-path reduction from this restructuring.
Notes: Post-quantum cryptography refers to cryptographic algorithms designed to resist attacks from quantum computers while still running on conventional computing systems. This is important because the cryptography does not itself require a quantum computer. NIST has already standardized ML-KEM for key encapsulation and ML-DSA and SLH-DSA for digital signatures. For our hardware accelerator, we are particularly interested in lattice-based cryptographic computation, especially the computational kernels associated with ML-KEM.

## Slide 11
Tests the NTT butterfly. It applies random/boundary values of a, b, and zeta.
It independently calculates:
It then compares these expected values against ntt_butterfly's a_out and b_out.
Tests the INTT butterflySimilarly verifies the inverse butterfly using:
This ensures the individual INTT butterfly operation follows the required modular arithmetic.
TB Uses 20,000 test vectors
It deliberately includes boundary cases such as 0, Q-1, and the previousl problematic:
a=100, b=50, zeta=2.
Arithmetic + NTT / INTT TB

## Slide 12
Arithmetic + NTT / INTT TB
Level 1: Arithmetic primitives
↓
mod_add/sub/mult
↓
Level 2: Butterfly primitives
↓
NTT / INTT butterfly
↓
Level 3: Transform engines
↓
Complete NTT / INTT
↓
Level 4: Adapters
↓
ntt_flat / intt_flat
↓
Level 5: ML-KEM accelerator
↓
Level 6: PicoRV32 + ML-KEM SoC

## Slide 13
Operation: Polynomial → NTT → INTT → Reconstructed Polynomial
Result: 0/256 coefficient mismatch
→ Round-trip PASSED
Round Trip
TB
Input:
256 known polynomial coefficients modulo 3329

## Slide 14
---------------------------------------------------------------
CROSS-CHECKS
---------------------------------------------------------------
CPU-reported mismatched words : 0
messages processed by CPU : 3 of 3
pipeline stage_done : 1111 (Dec Enc Key Exp)
seed reached the accelerator : bfbebdbcbbbab9b8b7b6b5b4b3b2b1b0afaeadacabaaa9a8a7a6a5a4a3a2a1a0
################################################################
# ML-KEM SoC DEMONSTRATION PASSED
# 3 messages encapsulated and decapsulated correctly
################################################################
Testbench → PicoSoC RAM → PicoRV32 → MMIO ML-KEM Accelerator → PicoRV32 → PicoSoC RAM → Testbench
SOC Demo Testbench